## Slide 1: Chapter 2 Processor Design

## Slide 2: Processor design
Processor design is about building the brain of a computer that can represent information and perform operations efficiently.

## Slide 3: Introduction
When you run a program, how does the processor actually understand numbers and perform calculations?

## Slide 4: Processor Organization (How CPU is structured)
Basic components:
ALU (Arithmetic Logic Unit) → performs calculations
Control Unit → directs operations
Registers → fast storage inside CPU
Buses → data movement pathways
Processor organization defines how these components are connected and work together.

## Slide 5: Information Representation
Before a processor computes anything, it must represent data in binary.
Key Concepts:
Binary numbers (0s and 1s)
Bits, bytes, words

## Slide 6: Number Formats
How does a computer represent negative numbers if it only understands 0 and 1?
A number format defines how numbers (positive, negative, fractional) are represented using binary.

## Slide 7: Number Formats
Integer Representation
Unsigned numbers
Signed numbers:
  Sign-magnitude
  1’s complement
  2’s complement (most important)

## Slide 8: Number Formats
Unsigned Binary Numbers
Concept:
Only non-negative numbers (0 and positive) are represented
All bits are used for magnitude
Example (4-bit):
Binary | Decimal
0000 | 0
0001 | 1
0101 | 5
1111 | 15

## Slide 9: Number Formats
Signed Number Representations
Unsigned cannot represent negative numbers—so we need signed formats.

## Slide 10: Number Formats
Signed Number Representations
Sign-Magnitude Representation
Concept:
MSB (Most Significant Bit) = sign
  0 → positive
  1 → negative
Remaining bits → magnitude
Example (4-bit):
Binary | Meaning
0101 | +5
1101 | -5

## Slide 11: Number Formats
Signed Number Representations
1’s Complement
Concept:
Negative number = invert all bits of positive number
Example:
+5 = 0101 -5 = 1010 (invert bits)

## Slide 12: Number Formats
Signed Number Representations
2’s Complement (Most Important)
Concept:
Negative number = invert bits + 1
Example: Represent -5 (4-bit)
Step 1: +5 = 0101 Step 2: Invert → 1010 Step 3: Add 1 → 1011
So, -5 = 1011

## Slide 13: Instruction
A processor cannot understand human language or even high-level programming languages. It only understands instructions in binary form.
An instruction is a command given to the CPU to perform a specific operation.
Example:
ADD A, B → Add contents of A and B
Internally → converted into binary machine code

## Slide 14: Basic Structure of an Instruction
Opcode (Operation Code) → What to do
Operand(s) → On which data
Example:
ADD A, B
Opcode → ADD
Operands → A, B

## Slide 15: Types of Instruction
1. Data Transfer Instructions
Purpose:
Move data from one place to another
Examples:
MOV A, B → Copy data from B to A
LOAD A, 1000 → Load data from memory address 1000
STORE A, 2000 → Store A into memory

## Slide 16: Types of Instruction
2. Arithmetic Instructions
Purpose:
Perform mathematical operations
Examples:
ADD A, B → A = A + B
SUB A, B → A = A - B
MUL A, B → A = A × B
DIV A, B → A = A ÷ B

## Slide 17: Types of Instruction
3. Logical Instructions
Purpose:
Perform bitwise operations
Examples:
AND A, B
OR A, B
NOT A
XOR A, B
Example (Binary):
A = 1010 B = 1100
AND → 1000
OR → 1110

## Slide 18: Types of Instruction
4. Control Flow Instructions
Purpose:
Change the normal sequence of execution
Examples:
JUMP 200 → Go to instruction at address 200
CALL FUNC → Call a function
RETURN → Go back after function ends
BRANCH if ZERO → Conditional jump

## Slide 19: Types of Instruction
Type | Purpose | Example | Analogy
Data Transfer | Move data | MOV A, B | Moving objects
Arithmetic | Calculate | ADD, SUB | Calculator
Logical | Bit operations | AND, OR | Filtering rules
Control Flow | Change execution | JUMP, CALL | Navigating a book
Summary

## Slide 20: Instruction
A program is nothing but a sequence of instructions, and these instruction types together enable the CPU to perform everything—from simple calculations to complex applications like AI or video processing

## Slide 21: Instruction
If a program had no control flow instructions, what would happen?

## Slide 22: Fixed-Point Arithmetic
What is Fixed-Point Arithmetic?
Fixed-point representation means numbers are stored in binary where the position of the decimal (binary point) is fixed.
It’s different from floating-point, where the decimal point “floats”

## Slide 23: Fixed-Point Arithmetic
How Numbers are Represented
Suppose we have n bits total. We decide how many bits are for the integer part and how many for the fractional part.
Example: Qm.n format
Qm.n → m bits for integer, n bits for fraction.
Total bits = m + n.
The binary point is always fixed after m bits.
🔹 Example (Q4.4 → 8-bit fixed-point):

## Slide 24: Fixed-Point Arithmetic
Fixed at 4th position
Suppose we have 8-bit numbers, and we decide:
First 4 bits = integer part
Last 4 bits = fractional part
So the binary point is always between bit 4 and bit 5:
xxxx.xxxx ← binary point fixed here

## Slide 25: Fixed-Point Arithmetic
Addition in Fixed-Point Arithmetic
Rule
Both numbers must be in the same fixed-point format (same number of integer and fractional bits).
Align the binary point.
Perform normal binary addition.
If result exceeds bit range → overflow occurs.

## Slide 26: Fixed-Point Arithmetic
Addition in Fixed-Point Arithmetic
Example – Q3.2 format (3 integer bits, 2 fractional bits)
iii.ff (total 5 bits: 3 integer + 2 fraction)
Add 3.25 and 1.75
Step 1: Convert to binary (Q3.2)
3.25 = 11.01₂ → 011.01
1.75 = 01.11₂ → 001.11
Step 2: Add
011.01 (3.25)
+ 001.11 (1.75)
-----------
101.00 (5.00)
Result = 5.0

## Slide 27: Fixed-Point Arithmetic
Example – Overflow Case
Add 7.50 and 2.75 in Q3.2 format
Step 1: Convert to Binary
7.50 = 111.10
2.75 = 010.11
Step 2: Add
111.10 (7.50)
+ 010.11 (2.75)
-----------
1010.01 (Invalid in Q3.2, overflow!)

## Slide 28: Fixed-Point Arithmetic
Fixed-Point Subtraction
Rule
Both numbers must be in the same fixed-point format.
Subtraction is usually performed using Two’s Complement:
A−B=A+(Two’s Complement of B)
Align the binary point.
Perform binary addition.
Check for overflow.

## Slide 29: Fixed-Point Arithmetic
Example – Q3.2 format (3 integer bits, 2 fractional bits)
Subtract 3.25 – 1.75
Step 1: Convert operands
3.25 = 11.01₂ → 011.01
1.75 = 01.11₂ → 001.11
Step 2: Take two’s complement of 001.11
Step 3: Add
001.11 → 110.01 (two’s complement)
011.01 (3.25)
+ 110.01 (-1.75)
----------
1001.10 → 001.10 (after ignoring carry)

## Slide 30: Fixed-Point Arithmetic
Fixed-Point Multiplication
Rule of Multiplication
Multiply the two binary numbers as integers (ignore binary point at first).
The binary point in the result is placed by adding the number of fractional bits from both operands.
If operands are in Qm.n and Qp.q → result is in Q(m+p).(n+q).
Overflow can occur if result needs more bits than available.

## Slide 31: Fixed-Point Arithmetic
Fixed-Point Multiplication
Example – Q3.2 × Q3.2
Multiply 1.50 × 0.75
Step 1: Convert numbers
1.50 = 01.10
0.75 = 00.11
Step 2: Multiply as integers (remove binary point)
0110 (decimal 6)× 0011 (decimal 3)= 00010010 (decimal 18)
Step 3: Adjust binary point
Each operand has 2 fractional bits → total 4 fractional bits.
So 00010010 → 0001.0010
Result = 1.125

## Slide 32: ALU Design
ALU is the core unit where all arithmetic and logical operations happen.
Operations:
Addition, subtraction
AND, OR, XOR
Comparisons

## Slide 33: Arithmetic Logic Unit (ALU)
What is ALU?
The Arithmetic Logic Unit (ALU) is the part of a microprocessor (or CPU) that performs mathematical (arithmetic) and decision-making (logic) operations

## Slide 34: Basic ALU Organization

## Slide 35: Floating-Point Arithmetic
Floating Point
The term “floating point” in floating-point arithmetic refers to the way numbers are represented, where the decimal (or binary) point “floats” rather than being fixed.

## Slide 36: Floating-Point Arithmetic
Fixed-point vs Floating-point
Fixed-point number: The decimal (or binary) point is at a fixed position. Example: 123.45 in a fixed-point system might always have 2 digits after the decimal.
Floating-point number: The decimal point can “float” to different positions depending on the magnitude of the number. Example:
  123.45 = 1.2345×102
  0.00123 = 1.23×10-3
In both cases, the mantissa stores the significant digits, and the exponent indicates where the decimal (or binary) point is.

## Slide 37: Floating-Point Arithmetic
Example : Simple Binary Floating Point Operation
Add : A=1.01×23, B=1.11×22
Step 1: Align exponents
A exponent = 3, B exponent = 2 → shift B right by 1 bit B = 0.111×23
Step 2: Add mantissas
1.01+0.111=10.001(binary)
Step 3: Normalize
10.001×23=1.0001×24
Result: R=1.0001×24

## Slide 38: Arithmetic Processors
If a CPU can already add and subtract, why do we need special arithmetic processors?

## Slide 39: Arithmetic Processors
Arithmetic processors are specialized hardware units designed to perform arithmetic operations (especially complex ones) faster and more efficiently than a basic ALU.
They are optimized for:
Speed
Parallelism
Precision

## Slide 40: Arithmetic Processors
Why Are Arithmetic Processors Needed?
Problem with Basic ALU
Handles simple operations well (ADD, SUB)
Slower for:
  Multiplication
  Division
  Floating-point operations

## Slide 41: Arithmetic Processors
Solution
Use dedicated hardware units:
Faster execution
Reduced CPU workload
Better performance for scientific and multimedia tasks

## Slide 42: Stack Processor
What is a Stack?
A stack is a data structure that follows:
LIFO (Last In, First Out)
Basic Operations:
PUSH → Insert data into stack
POP → Remove data from stack

## Slide 43: Stack Processor
Do we always need registers like A, B, C to perform operations?

## Slide 44: Stack Processor
A stack processor is a CPU design where all operations are performed using a stack instead of explicitly named registers.
Key point:
Operands are implicitly taken from the stack
Results are pushed back to the stack

## Slide 45: Stack Processor
Example :
Expression:
(A+B)×C
Step-by-step Execution: Stack Visualization:
PUSH A
PUSH B
ADD → (A+B)
PUSH C
MUL → (A+B) × C
Step | Stack
PUSH A | A
PUSH B | A, B
ADD | A+B
PUSH C | A+B, C
MUL | Result